# General License Examination – Memorization Sheet

General Class HF Frequency Privileges

10 meters	28000 – 29700 kHz

12 meters	24890 – 24990 kHz

15 meters	21025 – 21200 kHz and 21275 – 21450 kHz

17 meters	18068 – 18168 kHz

20 meters	14025 – 14150 kHz and 14225 – 14350 kHz (the last digits are 25-50, 25-50)

30 meters	10100 – 10150 kHz (CW and data only)

40 meters	7025 – 7125 kHz and 7175 – 7300 kHz

60 meters	5 authorized channels 2.8kHz wide within US

80 meters	3525 – 3600 kHz and 3800 – 4000 kHz

160 meters	1800 – 2000 kHz

Bolded items are in the question pool

Maximum 1500 watts PEP, Except  200 watts PEP on 30 meters, 100 watts for beacons

RTTY/data near center of CW allocation but LSB (170Hz shift for amateur RTTY)
80m data  3570-3600	20m RTTY  14.070-14.100 MHz	20m PSK31  14.070

Maximum Symbol Rate for Packet, RTTY, or Data

| Below 10 meters (28 MHz) | 300 baud | 6m and 2m | 19.6 kilobaud |
| --- | --- | --- | --- |
| 10 meter band | 1200 baud | 1.25m and 70cm | 56 kilobaud |

Use General privileges immediately with CSCE, add “/AG” to CW call and “Slant AG” on phone

Minimum Channel Separation
CW	150 – 500Hz	SSB	3 kHz

| Power Multipliers 20dB = 100 fold change One S-Unit = 6dB = 4 fold change 3dB = 2 fold change 1dB loss = -20.5% Propagation A-index – Long term geomagnetic stability | Data Modes PSK31 uses varicode RTTY uses 5 bit Baudot with 170Hz shift Sideband Operation Below 14 MHz use lower sideband (LSB) Above 14 MHz use upper sideband (USB) |
| --- | --- |

K-index – Short term geomagnetic stability

Solar Flux – Radio energy at 10.7cm

D layer absorbs, E layer max single hop ~ 1200 miles, F2 layer max single hop ~2500 miles

Low frequencies good at night (no D layer), higher HF work during day (good F layer charge)

Max range on frequency just below MUF, short range just above LUF

UV and X-rays take 8 minutes to arrive, coronal mass ejections (CMEs) take 20-40 hours

A two tone linearity test uses two non-harmonically related audio tones

Q-Signals and Prosigns

| QRP – Low power operation, ~ 5 watts on HF QRS – Send more slowly QRQ – Send faster QSL – Acknowledge receipt | QRV – Ready to receive KN – Listening for specific station(s) CL – Closing station AR – End of message |
| --- | --- |

Wire Sizes

15 amp circuit requires 14 gauge wire - 20 amp circuit requires 12 gauge wire

Series/Parallel	Series	Parallel

| Resistors/Inductors | Add - R1+R2+R3… | Divide - 1/ 1/(R1+1/R2+1/R3…) |
| --- | --- | --- |
| Capacitors | Divide - 1/ 1/(C1+1/C2+1/C3…) | Add - C1+C2+C3… |

Reactance

Increases with frequency in a coil, decreases with frequency in a capacitor

Impedance Matching

Matching impedance between source and load insures max power transfer/highest efficiency

Connectors

| DE-9 | Serial data | PL-259 | RF – Good to ~150MHz |
| --- | --- | --- | --- |
| DIN | Multiconductor audio/control | N | Waterproof RF – Good to ~10GHz |
| RCA | Audio | SMA | Small RF – Good to several GHz |

Components

| Field Effect Transistor | Zener Diode | NPN Transistor | Transformer | Tapped Inductor |
| --- | --- | --- | --- | --- |

| Germanium Diode Junction Threshold Voltage | 0.3 volts |
| --- | --- |
| Silicon Diode Junction Threshold Voltage | 0.7 volts |

Peak Envelope Power

PEP = [(0.707PEV)(0.707PEV)]/RL	Where:	PEV = Peak Voltage

RL = Resistive Load

Peak to Peak voltage= 2(Peak voltage)	RMS = .707(Peak voltage)

Ohm's Law and Power Formulas

E = Voltage in Volts

I = Current in Amperes

R = Resistance in Ohms

P = Power in Watts

Cover the value you need and divide or multiply the remaining values as appropriate

Examples:    P = I x E	P = I2 x R	P = E2 / R

Gates

| AND Gate | Output is high only when both inputs high |
| --- | --- |
| NOR Gate | Output is low when either or both inputs are high |

Antenna Lengths

| Dipole Length L (Ft) = 468 F (MHz) L is Length in Feet and F is Frequency in MHz | ¼λ Vertical L (Ft) = 234 F (MHz) Divide Full Wave Loop by 4 for one side of Quad Loop Divide Full Wave Loop by 3 for one side of Delta Loop |
| --- | --- |

3 element yagi maximum theoretical gain is 9.7dBi

# Text boxes

E

I

R

P

I

E

P

I2

R